## Slide 1
GPU Baseline
& Test Vectors
CS259 Final Project · Member A
NVIDIA TITAN V · FP16 single-head attention · S = 1K–16K

## Slide 2
What I built
1
Test vectors for the RTL team
INT8 matmul vectors for 4×4 / 8×8 / 16×16 arrays — 10 random + 3 edge cases each — plus a real GPT-2 attention tile. Ready to load with Verilog $readmemh.
2
GPU measurement pipeline
Latency, throughput (GFLOPS), memory traffic (Nsight Compute), power, energy, and GFLOPS/W, swept across sequence lengths 1K–16K. All results saved to CSV.

## Slide 3
Key results
16.3 TFLOPS
Peak throughput (S = 8192)
145 GFLOPS/W
Peak energy efficiency
9 – 491 mJ
Energy per inference (S = 1K → 16K)
Chart: Efficiency rises, then plateaus
| 1K | 2K | 4K | 8K | 16K
GFLOPS/W | 29.6 | 57.9 | 103.1 | 145.1 | 140

## Slide 4
Takeaway: the bar to beat
The GPU is far from its peak
It reaches only ~15% of the FP16 tensor-core peak; SM utilization stays at 5–38%. At this single-head, D=64 shape the GPU is underused and runs mostly from cache.
A baseline for the custom accelerator
At S = 4096 the GPU costs 41.7 mJ per inference at 103 GFLOPS/W. The systolic array (C/D) should aim to beat this energy efficiency on a fraction of the area.